## Slide 1
Concurrent Operation of Wireless Power Transfer Based Contactless Slip Ring and Motor Drive System with a Single Converter
Enes Ayaz
M.Sc. Thesis Defense
September 2022
Middle East Technical University (METU), Department of Electrical and Electronics Engineering Ankara, TURKEY
Notes: Dear professors and collagues

## Slide 2: Outline
Aim of Study
Wireless Power Transfer System Basics
Theory Of Operations
Implementation for DC Motor
Implementation for AC Motor
Implementation for field excitation
Conclusion

## Slide 3: Power Transfer to Rotating Frames
Slip Rings
Brushless Exciter
Contactless
Slip Rings

## Slide 4: Power Transfer to Rotating Frames
 | Slip Rings | Brushless Exciters | Contactless Slip Rings
Reliability | - | + | +
Maintenance | - | + | +
Simplicity | + | + | -
Speed Independency | + | - | +
Cost Effectivity | + | + | -
Efficiency | + | - | +

## Slide 5: Wireless Power Transfer Based Contactless Slip Rings
Tesla’s WPT System
 | Inductive Power Transfer | Capacitive Power Transfer
Transfer Type | Varying MF | Varying EF
Power Ratings | High | Low
Frequencies | Low | High
Efficiency | High | High
Distance | Moderate | Low

## Slide 6: Inductive Power Transfer
DC/AC converter
Compensation Circuits
Transmitter/Receiver Coils
AC/DC Rectifiers

## Slide 7: Conventional Inductive Power Transfer Based Contactless Slip Ring
Two converters:
  To drive the motor
  To excite the Tx coil
The WPT converter  generating high frequency
The motor drive  generating low and high frequency
Motor  attenuated in motor current
The WPT system behaves like band-pass filter
Motor  used to drive

## Slide 8: Proposed Inductive Power Transfer Based Contactless Slip Ring
The WPT converter  generating high frequency
The motor drive  generating high frequency
The WPT system behaves like band-pass filter
combining
eliminating

## Slide 9: Proposed Inductive Power Transfer Based Contactless Slip Ring
 | Conventional Contactless Slip Ring | Proposed Contactless Slip Rings
Reliability | + | +
Maintenance | + | +
Simplicity | - | +
Speed Independency | + | +
Cost Effectivity | - | +
Efficiency | + | +

## Slide 10: Outline
Aim of Study
Inductive Power Transfer System Basics
Theory Of Operations
Implementation for DC Motor
Implementation for AC Motor
Implementation for field excitation
Conclusion

## Slide 11: Inductive Power Transfer System

## Slide 12: Compensation Topologies
a) Series-series
b) Parallel-series
c) Series-parallel
d) Parallel-parallel
Series-Series Compensation | 
Source Type | Voltage Source
Resonant frequency | Load Independent
Resonant frequency | Coupling Independent
No load operation | Short Circuit
Capacitor Size | Large

## Slide 13: Series-Series IPT System
Single-peak band pass filter
First Harmonic Approach (FHA)
Phase < 0  Inductive region
 Inductive region

## Slide 14: Zero Voltage Switching
Inductive region  The capacitance of the switches discharges by the load current during dead time.

## Slide 15: Bifurcation Phenomenon
Make control difficult
Decrease efficiency
Double-peak
 Inductive region

## Slide 16: Multifrequency IPT Systems

## Slide 17: Outline
Aim of Study
Inductive Power Transfer System Basics
Theory Of Operations
Implementation for DC Motor
Implementation for AC Motor
Implementation for field excitation
Conclusion

## Slide 18: Compensation Topologies
 | Series-Series | Series-Parallel | Parallel-Parallel | Parallel-Series
Tx side Capacitor | Large | Large | Small | Small
Rx side Capacitor | Large | Small | Small | Large
No-load Operation | No | Yes | Yes | Yes
ω0 Load dependent | Independent | Dependent | Dependent | Dependent
ω0 Coupling dependent | Independent | Dependent | Dependent | Dependent
Source Type | VS | CS | CS | VS

## Slide 19
Slip Rings and Brushless Exciters
 | Slip Rings | Brushless Exciters | IPT Slip Ring
Merits | Inexpensive High electrical efficiency | No physical connection Reliable | No friction wear No speed limitation High efficiency Reliable
Challenges | Prone to failure due friction wear. Regular brush replacement Regular maintanence | Problematic at low rotational speed Expensive | Expensive Complex

## Slide 20
Inductive Power Transfer System Proposal
Modular structure is employed to increase:
  Reliablity
  Fault Tolerance
Receiver modules are connected in parallel to common DC-bus.

## Slide 21
Aim of Study
Inductive Power Transfer Systems
Analytical Modeling
Experimental Verification
2Tx-4Rx IPT System with Middle Stage Resonator
Conclusion
Outline

## Slide 22
Inductive Power Transfer System Topologies
 | Series-Series | Series-Parallel | Parallel-Parallel | Parallel-Series
Tx side Capacitor | Large | Large | Small | Small
Rx side Capacitor | Large | Small | Small | Large
No-load Operation | No | Yes | Yes | Yes
ω0 Load dependent | Independent | Dependent | Dependent | Dependent
ω0 Coupling dependent | Independent | Dependent | Dependent | Dependent
Source Type | VS | CS | CS | VS
Series-Series
Series-Parallel
Parallel-Parallel
Parallel-Series

## Slide 23
Zero Voltage Switching in IPT Systems
Leading power factor
Lagging power factor
For ZVS operation, lagging power factor
should be achieved!

## Slide 24
Bifurcation Phemonemon
Under bifurcation, operation above resonant frequency doesn’t guarentee ZVS operation!
Constant Rload - Variable magnetic coupling (k)
Constant magnetic coupling (k)- Variable Rload

## Slide 25
IPT Coil Shape Considerations
 | Same Direction (Circular) | Opposite Direction (Proposed)
Merits | Higher intrinsic quality factor. Easier to manufacture. | Significantly reduced Eddy losses on shaft Allows modular structures Easy mount and dismount of IPT coils
Challenges | High Eddy loss on rotating shaft. Doesn’t allow modular coil structures. | Less intrinsic quality factor. More turns for the same inductance Harder to manufacture

## Slide 26
Fundamental Harmonic Approximation(FHA)
1.3 dB
-27.5 dB
-33.5 dB

## Slide 27
Series-Series IPT Topology
No coupling(M=0)
0
0
0
No-load
No load operation is not allowed!
Zero coupling operation is not allowed!
High Q results in high voltage stress!

## Slide 28
Aim of Study
Inductive Power Transfer Systems
Analytical Modeling
Experimental Verification
2Tx-4Rx IPT System with Middle Stage Resonator
Conclusion
Outline

## Slide 29
Module Number Selection
 | 1Tx-1Rx | 1Tx-2Rx | 3Tx-3Rx | 2Tx-4Rx
Merits | Simple Constant coupling Constant Tx current | Constant coupling Constant Tx current Scalable | Allows 3-Φ systems Less semiconductor Higher control options | Same Tx currents Single Tx module operation Single Rx fault tolerant Scalable
Challenges | No load operation Fault tolerance | Tx module faults Current/power unbalance | Complex control | Complex Current/power unbalance Highest copper loss

## Slide 30
Analytical Design
Parameters | Value
 | 550 W
 | 500 W
 | 150 kHz
 | 100 V
 | 90
 | 100 V
 | 10 Ω
 | 16.21 Ω
 | 68.8 μH
 | 15 μH
 | 82 μH
 | 13.8 nF
 | Calculated later!
Parameters | Value
 | 550 W
 | 500 W
 | 150 kHz
 | 100 V
 | 100 V
 | 10 Ω
 | 16.21 Ω
 | 68.8 μH
 | 15 μH
 | 82 μH
 | 13.8 nF
 | Calculated later!
90% efficiency

## Slide 31
Current Balancing in Parallel Connected Common DC-Bus IPT Systems
Simulation results for equal magnetic coupling.()
Simulation results for unequal magnetic coupling.()
Phasor representation of equal(left) and unequal(right) coupling cases.

## Slide 32
Current Balancing Using Additional Cross-coupling
Simulation results for unequal coupling ()
without cross-coupling
Simulation results for unequal coupling ()
with cross-coupling

## Slide 33
Current Balancing Using Additional Cross-Coupling
Input |  | Output | 
 | 14.71 |  | 76.7°
 | 13.9 |  | 110.8°
 | 4.1 A | θ | 19.5°
 | 2.8 A |  | 11.02
Input |  | Output | 
 |  |  | 76.7°
 |  |  | 110.8°
 | 4.1 A | θ | 19.5°
 | 2.8 A |  | 
Mutual difference is given as 5%.

## Slide 34
Current Balancing Using Rx Module De-tuning
Simulation results for unequal coupling ()
without Rx module resonant frequency detuning()
Simulation results for unequal coupling ()
with Rx module resonant frequency detuning()

## Slide 35
Summary of Current Balancing Methods
Parameters | Value
 | 550 W
 | 500 W
 | 150 kHz
 | 100 V
 | 90
 | 100 V
 | 10 Ω
 | 16.21 Ω
 | 68.8 μH
 | 15 μH
 | 82 μH
 | 13.8 nF
(135 kHz) | 21 nF
 | 11 μH
Parameters | Value
 | 550 W
 | 500 W
 | 150 kHz
 | 100 V
 | 100 V
 | 10 Ω
 | 16.21 Ω
 | 68.8 μH
 | 15 μH
 | 82 μH
 | 13.8 nF
 | 21 nF
 | 11 μH

## Slide 36
Aim of Study
Inductive Power Transfer Systems
Analytical Modeling
Experimental Verification
2Tx-4Rx IPT System with Middle Stage Resonator
Conclusion
Outline

## Slide 37
Transmitter Side IPT Coil Design

## Slide 38
Receiver Side IPT Coil Design

## Slide 39
Ferrite Mass Reduction
 | Ferrite Back-core | Ferrite Spoke | 
Inductance | 80.9 μH | 65.4 μH | 20% Decrease
Ferrite Area | 669 | 207 | 69% Decrease
 | Ferrite Back-core | Ferrite Spoke | 
Inductance | 80.9 μH | 65.4 μH | 20% Decrease
Ferrite Area |  |  | 69% Decrease

## Slide 41
IPT Coil Finite Element Analysis
5% diffence
Remember current balancing analysis?

## Slide 42
Full Bridge Rectifier Modules

## Slide 43
Full Bridge Converter Design

## Slide 44
Full Bridge Converter Design-Additional Features

## Slide 45
Full Bridge Converter Design- Thermal Design

## Slide 46
Experimental Setup

## Slide 47
Current Balancing Experimental Results

## Slide 48
Rotational Experimental Results (Normal Operation)

## Slide 49
Rotational Experimental Results
(Single Rx-Open Fault Operation)

## Slide 50
Additional Experimental Results

## Slide 51
Aim of Study
Inductive Power Transfer Systems
Analytical Modeling
Experimental Verification
2Tx-4Rx IPT System with Middle Stage Resonator
Conclusion
Outline

## Slide 52
2Tx-4Rx IPT System with Middle Stage Resonator

## Slide 53
Analytical Design

## Slide 54
2Tx-4Rx IPT System with Middle Stage Resonator

## Slide 55
2Tx-4Rx IPT System with Middle Stage Resonator
Normal Operation
Single Rx Open Circuit
Fault
Double Rx Open Circuit
Fault

## Slide 56
2Tx-4Rx IPT System with Middle Stage Resonator
Single Tx Open Circuit
Fault

## Slide 57
2Tx-4Rx Rotational IPT System with Middle Stage Resonator

## Slide 58
2Tx-4Rx Rotational IPT System with Middle Stage Resonator

## Slide 59
2Tx-4Rx Rotational IPT System with Middle Stage Resonator

## Slide 60
2Tx-4Rx Rotational IPT System with Middle Stage Resonator

## Slide 61
Aim of Study
Inductive Power Transfer Systems
Analytical Modeling
Experimental Verification
2Tx-4Rx IPT System with Middle Stage Resonator
Conclusion
Outline

## Slide 62
Comparison

## Slide 63
Contribution to Literature and Novelties

## Slide 64
Thanks!