## Slide 1
A set of Wireless and Wired Power Transfer Systems
Studies
Enes Ayaz
10/01/2023

## Slide 3: Previously on the 30-min Presentation
Motivations:
To increase DC-link utilization rate
To increase power
To break the restrictions
Motor drives have more than 2 wires
Conventional WPT systems have 2 wires input
Multi-phase WPT systems
Notes: The WPT system is connected between phase-A and phase B.
By carrier phase shift to phase B, we achieve this contour of the magnitude of the switching frequency.
We can observe that we can have a constant gain for any modulation.
The constant gain is between 0.25 and 0.45 over a DC-link voltage.
The control diagram is shown.
We adjust the carrier phase shift according to modulation to control the WPT power.

## Slide 4: Future Works
Notes: The WPT system is connected between phase-A and phase B.
By carrier phase shift to phase B, we achieve this contour of the magnitude of the switching frequency.
We can observe that we can have a constant gain for any modulation.
The constant gain is between 0.25 and 0.45 over a DC-link voltage.
The control diagram is shown.
We adjust the carrier phase shift according to modulation to control the WPT power.

## Slide 5: Challenge- Calculation Burden!
Notes: The WPT system is connected between phase-A and phase B.
By carrier phase shift to phase B, we achieve this contour of the magnitude of the switching frequency.
We can observe that we can have a constant gain for any modulation.
The constant gain is between 0.25 and 0.45 over a DC-link voltage.
The control diagram is shown.
We adjust the carrier phase shift according to modulation to control the WPT power.

## Slide 6: Variable Carrier Phase Shift Method for Integrated Contactless Field Excitation System of Electrically Excited Synchronous Motors
The circuit diagram of a conventional and proposed CFE based on a WPT system for EESMs.
a) The conventional system. b) The proposed system.
The circuit diagram of the proposed system
Notes: The WPT system is connected between phase-A and phase B.
By carrier phase shift to phase B, we achieve this contour of the magnitude of the switching frequency.
We can observe that we can have a constant gain for any modulation.
The constant gain is between 0.25 and 0.45 over a DC-link voltage.
The control diagram is shown.
We adjust the carrier phase shift according to modulation to control the WPT power.

## Slide 7: Variable Carrier Phase Shift- Time Domain Analysis

## Slide 8: Multifrequency IPT Systems
Motivations:
To Increase power
To reduce switching components
To increase DC-link utilization rate
To provide operation for more than one standards
Some Topologies:
Multi-converter and multi-resonant
Single-converter and multi-resonant
Single-converter and multi-load
Standards:
Wireless Power Consortium (WPC)
Power Matters Alliance (PMA)
Alliance for Wireless Power (A4WP)
100 - 205/300 kHz for magnetic resonant and induction technology for mobile devices; WPT systems for consumer devices, power transfer typically < 200 W; plan to be used worldwide
6765 - 6795 kHz for magnetic resonant technology for mobile devices; WPT systems for consumer devices, power transfer typically < 30 W; plan to be used.
300 - 500 kHz: WPT systems for consumer devices, power transfer typically < 5 W; plan to be used for smaller devices.
900 - 1 000 kHz: WPT systems for consumer devices, power transfer typically < 5 W; plan to be used for smaller devices.
Notes: The WPT system is connected between phase-A and phase B.
By carrier phase shift to phase B, we achieve this contour of the magnitude of the switching frequency.
We can observe that we can have a constant gain for any modulation.
The constant gain is between 0.25 and 0.45 over a DC-link voltage.
The control diagram is shown.
We adjust the carrier phase shift according to modulation to control the WPT power.

## Slide 9: Narrowband Concurrent Wireless Power Transfer (For use of single standard range)
A Dual-Frequency Three-Dimensional WPT System with Directional Power Transfer
Capability at Two Separately Regulated Outputs
Notes: The WPT system is connected between phase-A and phase B.
By carrier phase shift to phase B, we achieve this contour of the magnitude of the switching frequency.
We can observe that we can have a constant gain for any modulation.
The constant gain is between 0.25 and 0.45 over a DC-link voltage.
The control diagram is shown.
We adjust the carrier phase shift according to modulation to control the WPT power.

## Slide 10: Narrowband Concurrent Wireless Power Transfer (For use of single standard range)
Design and Control of a Decoupled Multichannel Wireless Power Transfer System Based on Multilevel Inverters

## Slide 11: Narrowband Concurrent Wireless Power Transfer
Multi-Frequency Multi-Amplitude Superposition Modulation Method With Phase Shift Optimization for Single Inverter of Wireless Power Transfer System

## Slide 12: Wideband Concurrent Wireless Power Transfer
Multi-Frequency Multi-Amplitude Superposition Modulation Method With Phase Shift Optimization for Single Inverter of Wireless Power Transfer System

## Slide 13: Narrowband / Wideband Concurrent Wireless Power Transfer
GaN-Based Dual-Mode Wireless Power Transfer Using Multifrequency Programmed Pulse Width Modulation

## Slide 14: Narrowband and Wideband Concurrent Wireless Power Transfer using a Single Transmitter
SPWM
Notes: The WPT system is connected between phase-A and phase B.
By carrier phase shift to phase B, we achieve this contour of the magnitude of the switching frequency.
We can observe that we can have a constant gain for any modulation.
The constant gain is between 0.25 and 0.45 over a DC-link voltage.
The control diagram is shown.
We adjust the carrier phase shift according to modulation to control the WPT power.

## Slide 15
Wideband Concurrent Wireless Power
Control parameters :
Modulation index
Carrier phase shift

## Slide 16
Narrowband Concurrent Wireless Power
Control parameters :
Modulation index
Carrier phase shift
Fundamental phase shift

## Slide 17
Additional Narrowband/Wideband Concurrent Wireless Power for HB configuration
HB:
It is not possible to introduce carrier or fundamental phase shifts
Control parameters :
Fundamental modulation index
Harmonic modulation index (3rd , 5th , 7th )
Narrow Band
Wide Band

## Slide 18: Balancing with Soft-Magnetic Material based Inductors
Intentional de-tuning of the receiver resonant tank for unbalanced modules
Notes: The WPT system is connected between phase-A and phase B.
By carrier phase shift to phase B, we achieve this contour of the magnitude of the switching frequency.
We can observe that we can have a constant gain for any modulation.
The constant gain is between 0.25 and 0.45 over a DC-link voltage.
The control diagram is shown.
We adjust the carrier phase shift according to modulation to control the WPT power.

## Slide 19: Balancing with Soft-Magnetic Material based Inductors
Notes: The WPT system is connected between phase-A and phase B.
By carrier phase shift to phase B, we achieve this contour of the magnitude of the switching frequency.
We can observe that we can have a constant gain for any modulation.
The constant gain is between 0.25 and 0.45 over a DC-link voltage.
The control diagram is shown.
We adjust the carrier phase shift according to modulation to control the WPT power.

## Slide 22: Soft-Magnetic Material based Inductors
Requirement
  Saturable Core
  Excitation Circuit
  Trap Filter
Cost, Size comparison
Notes: The WPT system is connected between phase-A and phase B.
By carrier phase shift to phase B, we achieve this contour of the magnitude of the switching frequency.
We can observe that we can have a constant gain for any modulation.
The constant gain is between 0.25 and 0.45 over a DC-link voltage.
The control diagram is shown.
We adjust the carrier phase shift according to modulation to control the WPT power.

## Slide 24: Soft-Magnetic Material based Inductors without additional converter

## Slide 26: Future Works
1- Synchronous motor journal : Written, but some experimental results are needed.
2- Preparing Wide/narrow bandgap wireless power transfer journal draft :
  Literature Review (almost made)
  Analytic modelling :
    SPWM is ready
    SPWM with additional harmonic is standing
  Experimental setup:
    Find Of-the-shelf inductance for the story
    Power is about 30W to 5W
    6.78 MHz with 80kHz-200kHz or 900kHz-1000kHz with 80kHz-200KHz
3-Preparing Balancing journal draft ( we can focusTPEL special section about high power and misalingment)
Discussions to get into focus
    High power, series/parallel connection
    Cost and feasibility
Notes: The WPT system is connected between phase-A and phase B.
By carrier phase shift to phase B, we achieve this contour of the magnitude of the switching frequency.
We can observe that we can have a constant gain for any modulation.
The constant gain is between 0.25 and 0.45 over a DC-link voltage.
The control diagram is shown.
We adjust the carrier phase shift according to modulation to control the WPT power.

## Slide 27
Thanks!